## Slide 1
BU90003GWZEVK-101 Measurement Report
March 4th, 2014
Hosted by: Xuan Dang

## Slide 2
Equipment list
Regulated DC Power Supply
  QJE QJ3005XE (0-30V/5A)
Multimeter:
  Fluke 87V True RMS
  Fluke 106
Oscilloscope
  Rigol DS1102E
Electronic Load
  B&K BK8500
Current probe
  RP1001C

## Slide 3
Functional Test
Test case 1 procedure
  Connect DC Supply to: [+]VIN(TP1) and [-]GND(TP2) when EN is off. Set output of DC Supply in range from 2.3V to 5.5V and turn it on.
  Connect Electronic Load to: [+]VOUT(TP3) and [-]GND(TP4). Power on Electronic Load, set input of Electronic Load to 1A and turn on load.
  Move J1 header to turn EN on.
Result:
VIN = 2.3V to 5.5V
VOUT = 1.18V/1A (in both modes, Automatic PFM/PWM and Automatic PFM/PWM). Test passed.

## Slide 4
Functional Test (cont.)
Test case 2 procedure
  After implement test case 1, the IC operate properly.
  Move J1 header to turn EN off.
  Move J1 header to turn EN on.
Result:
VIN = 5V.
VOUT = 0.27V/1A (in both modes, Automatic PFM/PWM and Automatic PFM/PWM). Test failed.
IOUT 0.25A/Div. (DC)
VOUT 100mV/Div. (DC)

## Slide 5
Functional Test (cont.)
Test case 3 procedure
  After implement test case 1, the IC operate properly.
  Turn off DC Supply.
  Turn off load( don’t power off Electronic Load).
  Move J1 header to turn EN off.
  Turn on load.
  Turn on DC Supply.
  Move J1 header to turn EN on.
Result:
VIN = 5V.
VOUT = 0.27V/1A (in both modes, Automatic PFM/PWM and Automatic PFM/PWM). Test failed.
IOUT 0.25A/Div. (DC)
VOUT 100mV/Div. (DC)

## Slide 6
Functional Test (cont.)
Test case 4 procedure
  Connect DC Supply to: [+]VIN(TP1) and [-]GND(TP2) when EN is off. Set output of DC Supply in range from 2.3V to 5.5V and turn it on.
  Connect Electronic Load to: [+]VOUT(TP3) and [-]GND(TP4). Set input of Electronic Load to 1A and don’t turn on load.
  Move J1 header to turn EN on when load is still off.
  Turn on load.
Result:
VIN = 2.3V to 5.5V
VOUT = 1.18V/1A (in both modes, Automatic PFM/PWM and Automatic PFM/PWM). Test passed.

## Slide 7
Functional Test (cont.)
Test case 5 procedure
  After implement test case 1, the IC operate properly.
  Turn off load.
  Turn on load.
Result:
VIN = 2.3V to 5.5V
VOUT = 1.18V/1A (in both modes, Automatic PFM/PWM and Automatic PFM/PWM). Test passed.

## Slide 8
Hot Plugging Test
Test condition
  VIN = 5.5V
  IOUT = 1A
  With original diode D1: P4SMA6.8A
Result:
IIN MAX= 13.2A
VIN peak transient voltage (in both modes) is 7.68V > VIN Maximum Rating (7V)
VIN 2V/Div. (DC)
IIN 3A/Div. (AC)

## Slide 9
Circuit Quiescent Current Measurement
Test condition
  VIN = 0-5.5V
  Automatic PFM/PWM Mode
  Room temperature 25oC
Chart: VCC (V)
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5 | 5.25 | 5.5
ICC With P4SMA6.8A | 0 | 0.2 | 0.3 | 0.6 | 46.5 | 260.9 | 484.8 | 658 | 751 | 43 | 43.9 | 45 | 46 | 47.5 | 49 | 51 | 53.5 | 56 | 59.9 | 64 | 70 | 79 | 91

## Slide 10
Circuit Quiescent Current Measurement (cont.)
Test condition
  VIN = 0-5.5V
  Forced PWM Mode
  Room temperature 25oC
Chart: VCC (V)
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5 | 5.25 | 5.5
ICC With P4SMA6.8A | 0 | 0.2 | 0.3 | 0.8 | 52 | 265 | 489 | 660 | 753 | 5140 | 5210 | 5300 | 5430 | 5530 | 5640 | 5760 | 5910 | 6060 | 6230 | 6400 | 6590 | 6780 | 7010

## Slide 11
Efficiency Measurements
Test condition
  VIN = 5V
  VOUT = 3.3V
  Room temperature 25oC
Chart: IOUT (mA)
| 0 | 1 | 10 | 50 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
Automatic PFM/PWM Mode | 0 | 39.2 | 72.3 | 79.9 | 82 | 81.8 | 81.9 | 81.2 | 80.3 | 79 | 77.1 | 75.3 | 73.7 | 71.8
Forced PWM Mode | 0 | 3.6 | 27.1 | 63 | 74.5 | 80.9 | 81.7 | 81.3 | 80.2 | 79.1 | 77.4 | 75.3 | 73.7 | 71.8

## Slide 12
Load Response Measurements
Load response characteristic
(VIN=5V, VOUT=1.2V, IOUT=0  1A, Automatic PFM/PWM Mode)
VOUT 50mV/Div. (AC)
IOUT 0.5A/Div. (DC)

## Slide 13
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=1.2V, IOUT=1A  0, Automatic PFM/PWM Mode)
VOUT 50mV/Div. (AC)
IOUT 0.5A/Div. (DC)

## Slide 14
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=1.2V, IOUT=0  1A, Forced PWM Mode)
VOUT 10mV/Div. (AC)
IOUT 0.5A/Div. (DC)

## Slide 15
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=1.2V, IOUT=1A  0, Forced PWM Mode)
VOUT 10mV/Div. (AC)
IOUT 0.5A/Div. (DC)

## Slide 16
Ripple Response Measurements
VOUT Ripple voltage
(VIN=5V, VOUT=1.2V, IOUT=1A, Automatic PFM/PWM Mode and Forced PWM Mode)
VSW 2V/Div. (DC)
VOUT 10mV/Div. (AC)

## Slide 17
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=5V, VOUT=1.2V, IOUT=10mA, Automatic PFM/PWM Mode)
VSW 2V/Div. (DC)
VOUT 20mV/Div. (AC)

## Slide 18
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=5V, VOUT=1.2V, IOUT=10mA, Forced PWM Mode)
VSW 2V/Div. (DC)
VOUT 10mV/Div. (AC)

## Slide 19
Input Voltage Ripple Measurements
VIN Ripple voltage
(VIN=5V, VOUT=1.2V, CIN=4.7uF + 0.1uF, IOUT=0A, Automatic PFM/PWM Mode)
VIN 10mV/Div. (AC)

## Slide 20
Input Voltage Ripple Measurements (cont.)
VIN Ripple voltage
(VIN=5V, VOUT=1.2V, CIN=4.7uF + 0.1uF, IOUT=1A, Automatic PFM/PWM Mode)
VIN 50mV/Div. (AC)

## Slide 21
Input Voltage Ripple Measurements (cont.)
VIN Ripple voltage
(VIN=5V, VOUT=1.2V, CIN=4.7uF + 0.1uF, IOUT=0A, Forced PWM Mode)
VIN 10mV/Div. (AC)

## Slide 22
Input Voltage Ripple Measurements (cont.)
VIN Ripple voltage
(VIN=5V, VOUT=1.2V, CIN=4.7uF + 0.1uF, IOUT=1A, Forced PWM Mode)
VIN 50mV/Div. (AC)